## Slide 1: Google SketchUp Kurs: Principi CAAD-a, Predavanje 03 Univerzitet u Beogradu, Arhitektonski fakultet
Dr Mirjana Devetaković
Beograd, 2013
Podela linije
Ortogonalni i radijalni nizovi
Layer-i
Kote
Stilovi prikaza i materijali
Kontrola senke
Preseci
Grupe i komponente
Komentar zadatka 02
Zadatak 03

## Slide 2
Princip 01: Dinamičan razvoj CAAD-a
Princip 02: Približavanje korisniku
Princip 03: Slika kao sredstvo saopštavanja arhitektonske ideje
Princip 04: Preciznost
Princip 05: Brzina
Princip 06: Efikasnost u izmenama tokom procesa projektovanja
Princip 07: Crtež kao document i sredstvo saopštavanja arhitektonske ideje
Princip 08: Objektno orijentisani CAAD
Princip 09: Model kao sistem informacija i sredstvo saopštavanja arhitektonske ideje
Princip 10: BIM Building Information Modeling 1
Princip 11: Interoperabilnost
Princip 12: NURBS modeliranje
Princip 13: Matematičko definisanje kompleksne forme
Princip 14: Parametarsko modeliranje
Princip 15: Fabrikacija
> Principi

## Slide 3
> Komande za crtanje i modifikaciju
> Precizan unos veličina
> Vezivanje unosa za koordinatne ose, postojeće tačke i pomoćne linije

## Slide 4
> Komande za crtanje (Draw)
Rectangle
Line
Circle
Arc
Polygon
Freehand Tool

## Slide 5
> Komande za modifikaciju (Modify/Edit)
Move
Rotate
Scale
Pull/Push
Follow Me
Offset

## Slide 6
> Precizan unos veličina
Podešavanje jedinica
Window – Model info - ...
Unos veličina
Imenovane veličine: 5m, 37cm, 528mm, 4’
Apsolutne koordinate [x, y, z]
Relativne koordinate <x, y, z>
Arrays (Move/Copy, Rotate), Arc, Line, Circle, Offset, Polygon...

## Slide 7
> Vezivanje za kontekst (Inference)

## Slide 8
Arrays
An array is an arrangement of geometry in a line (linear array) or around an point (radial array).
number + x (external array). Type this number after making a manual copy of geometry to duplicate that copy an additional x-1 times. So, 3x creates 2 additional copies plus the original copy. The copies are made in the same direction as the first copy (either in a line or radially around a point). Example: 3x
number + * (external array) Type this number after making a manual copy of geometry to duplicate that copy an additional x-1 times. So, 3* creates 2 additional copies plus the original copy. The copies are made in the same direction as the first copy (either in a line or radially around a point). Example: 3*
/ (internal array). Type this number after making a manual copy of geometry to duplicate copy an additional x-1 times (between the original and manual copy). So, 3/ creates 2 additional copies between the original and manual copy. The copies are made moving backward from the first, manual, copy (either in a line or radially around a point). Example: 3/
http://support.google.com/sketchup/bin/answer.py?hl=en&answer=151558

## Slide 10
> Podela linije
Linija (ivica) se deli tako što se selektuje i aktivira kontekst-meni u kome se nalazi opcija Divide
Pomeranjem kursora duž linije, povećava se i smanjuje broj segmenata i kontroliše se njihova dužina

## Slide 11
> Stilovi prikaza

## Slide 12
> Materijali

## Slide 13
> Kontrola senke

## Slide 14
> Kote podešavanje (Window, Model Info, Units/Dimensions)

## Slide 15
> Layer-i
Color by layer
Entity info
Pomoću Layer-a se kontroliše vidljivost entiteta, ali ne i uticaji na njihovu geometriju.

## Slide 16
Layer on/off
Move
> Layer-i

## Slide 17
> Sticky geometry
> Grupe
> Komponente

## Slide 18
> “Sticky” geometrija
Move point
Push
Rectangle
Rectangle / Push
Move edge
Move edge
Move edge
Select edge
Move face
Select face
Move face
Select face

## Slide 19
> Group

## Slide 20
> Components

## Slide 21
> Components
Insert (Component from Warehouse)
Edit - Make Component

## Slide 22
> Preseci

## Slide 23
> Preseci (Sections)

## Slide 24
> Preseci (Sections) Create group from slice
Section cuts on-off Create group from slice
Move group; Explode

## Slide 25
> Zadatak Varijacije Na temu KOCKA

## Slide 26
> Zadatak
Zadatak 02 – Koristeći poznate komande u programu SketchUp, napraviti seriju varijacija na temu KOCKA, kao u datom primeru. Dimenzije inicijalne kocke 10/10m. Kao odgovor na ovaj zadatak napraviti 2 referentna prikaza veličine 200/200 piksela i priložiti izvornu datoteku .skp. U tekstu dati komentar koji ukratko objašnjava postupak crtanja.
Za odgovor na ovaj zadatak predviđeno je 7 dana. Svaki zadatak nosi do 10 poena. Procenat koji će neki zadatak imati u ukupnom broju poena predviđenom za kvalitet redovnog rada, biće određen naknadno.
Svaki zadatak nosi do 10 poena. Procenat koji će neki zadatak imati u ukupnom broju poena predviđenom za kvalitet redovnog rada, biće određen naknadno.

## Slide 28
Damjana Lojanicic

## Slide 29
Uroš Pajović

## Slide 30
Jelena Janković

## Slide 31
Jelena Janković

## Slide 32
Miljan Salata

## Slide 33
Nikola Jovanović

## Slide 34
Martina Milić

## Slide 35
Maja Udilović

## Slide 36
Saša Dimitrić

## Slide 37
Saša Dimitrić

## Slide 38
> Zadatak 02 - komentar KOCKA inspirisana kolekcijom IENAMI

## Slide 43
> Zadatak Model svetionika prema izabranom primeru

## Slide 44
Zadatak 03 – U literaturi ili na Internetu pronaći referentan primer svetionika (lighthouse, phare, Leuchtturm, маяк). Koristeći program SketchUp napraviti što verniji model ovog objekta. U prilogu postaviti fotografiju izabranog objekta, kao i dva prikaza modela. Veličina ilustracija 200/200 piksela...
Svaki zadatak nosi do 10 poena. Procenat koji će neki zadatak imati u ukupnom broju poena predviđenom za kvalitet redovnog rada, biće određen naknadno.
> Zadatak

## Slide 45
> Test

## Slide 46
http://sketchup.google.com/3dwarehouse/
> References
http://sketchup.google.com/intl/en/training/videos.html